Population estimates of Kibera slums in 2009

Nairobi – Kenya

Figure1: Kibera slum

Table of contents

1.	Basic Data and image preprocessing	4

VHRS image	4

Image preprocessing	4

2.	Building extraction on basis of digitization	6

3.	Change detection analysis	7

Change detection	7

Combination of the red bands	7

Manual interpretation	9

4.	Field survey and interpretation of results	10

Survey method	10

Interpretation of results	12

	Population estimate for the whole Kibera	13

	Population estimate based on individual village estimates	14

	Population estimates based on the extrapolation of KIANDA results	15

Results summary	18

Conclusion:	19

Kibera is one of the biggest informal settlements in the world where people live in a extremely dense urban context.

One of the major issues concerning slums is the population estimates since most of them are outdated or difficult to obtain considering the difficulty to monitor such places.

Yet, it is necessary to get as precise an estimate as possible in order to address basic services as medical care or water and sanitation equipment. Having a good estimate of the population number and comparing it to persons having access to medical care will help improving the planning of MSF’s acitivities.

Several demographic projects have being carried over Kibera with no probing results since the population number is still wavering between 350.000 and 1 million inhabitants. The issues to be tacked with are the extreme density of buildings and people that turns the place into a maze, the disturbing political question that is the reason for vague population census in slums and the time consuming and costly procedure that a proper census would represent.

An alternative to this is the combined use of very high satellite imagery and sample field survey. Satellite imagery will serve as a basis for support mapping to field inquiries. MSF   proceeded through simple random sampling of Kibera structures to obtain representative population data . An average population estimate will be computed for the selected zones and extrapolated to the full Kibera extent.

The project presents 4 phases:

- Data acquisition - Quickbird archive imagery from 2009-02-19 over Kibera for update survey. A former acquisition over Kibera was made in 2004-02-14 for MSF in the context of the HUMAN project to locate MSF-B activities.  Preprocessing of raw data

- Digitization of buildings within Kibera boundaries in order to support field survey and to identify the inhabited proportion.

- Change detection analysis between 2004 and 2009 in order to indentify expanding built-up areas, removal of buildings, any change or absence of change that can help interpret the population dynamics.

- Field survey and extrapolation of population estimates to the whole Kibera.

# Basic Data and image preprocessing

## VHRS image

Quickbird images from 2009-02-19 and 2004-02-14 were provided to MSF as natural colour image with a resolution of 0.6m.

## Image preprocessing

- Pansharpening (fusion between 0.6m panchromatic image and 2.4 colour image)

Figure 2: Pansharpening technique and image improvement.

Image Source © 2004 DigitalGlobe, Inc. All Right Reserved

- Georeferencing using RPC included in original data file and based on Quickbird image from 2009-02-02.

Kibera 2004 – Quickbird from 2004/02/14

Kibera 2009 - Quickbird from 2009/02/19

# 2.  Building extraction on basis of digitization

Buildings were interpreted and extracted manually since in this dense urban context automatic extraction is not performant.

Figure3: Visual interpretation and digitization of slum structures on basis of Quickbird image

# 3.  Change detection analysis

Has Kibera grown or densified? Where are the extension zones located? What changes occurred between 2004 and 2009 in Kibera? Are they identifiable on the satellite imagery?

Urban extensions on the outskirts of the slum are clearly visible, as well as changes in the pattern (road drawing…), new buildings, clearing of areas…

The comparison of both situation were made according to 3 methods, 2 semi-automatic methods using ENVI 4.5 and one manual method in ArcGIS.

## Change detection

The software computes automatically the difference between both images to identify areas where the urban morphology changed and where it remained identical.

Figure4: Evolving urban morphology in red

In red, were changes occurred, in white where it remained identical. This solution requires some cleaning afterwards because a lot of artifacts are generated due to the imperfect superimposition of both images.

## Combination of the red bands

The red bands from both images were combined in an RGB file in order to point out the changes that occurred in the urban landscape.

| Kibera – South West (Raila village) - 2004/02/14 Part of Raila village was bulldozed on 2004/02/08 and more than 1000 people evicted by the authorities | Kibera – South West (Raila village) - 2009/02/19 | In red, the urban extension since 2004. Combination of the red band of both images from 2004 and 2009 |
| --- | --- | --- |
|  | Light blue - No change |  | Red – vegetation that was present in 2004 disappeared to the benefit of buildings |
|  | Light blue - No change |  | Light red – buildings were here in 2004 but roofs have been changed, renewed or are brighter |
|  | Red - Urban extension 2009 – Kibera outskirts |  | Light red – buildings were here in 2004 but roofs have been changed, renewed or are brighter |
|  | Dark red – new buildings within Kibera boundaries |  | Dark blue – the blue stain here corresponds to a new round building with a darker roof. |
|  |  |  | Dark blue - buildings were here in 2004 but roofs have been changed, renewed or are brighter |

In general, light blue means no change, red and red hues show new buildings since 2004 and/or buildings with new bright roofs and dark blue shows new buildings that have darker roofs.

This semi-automatic change detection provides a first rapid visualization of the changes that have occurred between 2004 and 2009. But the result is quite complicated to interpret.

## Manual interpretation

For clarity purpose, a third solution was adopted to cope with the artifacts of the semi-automatic solution. This manual solution implies filling in the attribute table of the digitized buildings in order to symbolize new constructions and buildings that were pulled down.

Figure5: Evolution of the structures of the slum – urban extension / clearance, building modification

Remark:

New buildings are essentially located on the outskirts of Kibera, namely in Raila village in the South West where there is no limitation by either river or pond (South), other urbanized area (North West and East), golf course (North).

# 4. Field survey and interpretation of results

## Survey method

Given the time and budget constraints, the field survey had to be well defined. The method used was a random sampling method that selected 500 structures identified by the Structure ID from the shapefile. Because of -doubles and inaccurate structures, only 482 remained.

The field survey was carried out by a group of MSF trained casual workers using maps based on the digitization. 6 teams of 2 persons each were trained and conducted the survey, visiting the selected structures in order to identify their function, the number of units and number of people living by structure. Most of the Kibera structures are divided into separate units (mostly made up of 1 single room, but sometimes more) in which different households live.

The slum is composed of 13 villages: Gatwekera, Kanbimuru, Kianda, Kisumu Ndogo, Laini Saba, Lindi, Makina, Mashimoni, Raila, Silanga, Soweto East, Soweto West Kicchinjio is not a separate village, administratively it is part of Makina. In our study, we added the fringe of slum structures bordering the railway in the neighbouring villages of Olympic and Karanja. ( could we alter the map below slightly, the small and separate bit that's North West of Makina is actually not part of Makina. It is Toi Market, so can we rename that bit Toi instead of Makina?

Figure7: Kibera villages

In the end, 482 structures were visited randomly throughout the slum for a total of 1917 units. Structures correspond to digitized features or roofs that may cover several units. 188 units were identified as non residential units, 1678 as residential units that were visited and 51 remaining units that were not visited. The average number of people per unit amounts to 2.8persons while the total number of inhabitants for the 482 structures visited amount to 5360 persons.

Figure8: 482 structures randomly chosen for the field survey

Considering those figures, we can extrapolate population estimates for the entire slum of Kibera.

The results were transferred for analysis and extrapolation in xls and Access format (see POP_KIBERA_SIG.xls and KIBERA_SURVEY_2.mdb).

Thanks to the digitization and field survey, we benefit from 4 levels of analyses possible based on the assessment of the population per

- Number of structures

- Structure surface or inhabited area

- Kibera “administrative” area

- Individual villages “administrative” area

It will be interesting to exploit the different levels of analyses to compare them.

## Interpretation of results

Results from the field survey

| TEST SITES | Nb of Structures | Nb of units | Area of structures (ha) | Average nb of inhabitants/ structure | Nb of inhabitants |
| --- | --- | --- | --- | --- | --- |
| Gatwekera | 55 | 212 | 0.42 | 12 | 641 |
| Kanbimuru | 20 | 57 | 0.17 | 8 | 151 |
| Karanja | 0 | 0 | 0 | 0 | 0 |
| Kianda | 42 | 166 | 0.28 | 13 | 559 |
| Kisumu Ndogo | 29 | 163 | 0.31 | 19 | 538 |
| Laini Saba | 64 | 168 | 0.40 | 5 | 331 |
| Lindi | 57 | 175 | 0.37 | 10 | 551 |
| Makina | 59 | 270 | 0.56 | 13 | 747 |
| Mashimoni | 21 | 115 | 0.17 | 15 | 315 |
| Olympic | 4 | 4 | 0.0357 | 0 | 0 |
| Raila | 21 | 49 | 0.10 | 8 | 158 |
| Silanga | 46 | 223 | 0.40 | 10 | 455 |
| Soweto East | 39 | 193 | 0.34 | 12 | 474 |
| Soweto West | 25 | 122 | 0.18 | 18 | 439 |
| TOTAL | 482 | 1917 | 3.73 | 11 | 5359 |

### Population estimate for the whole Kibera

#### Number of inhabitants per general “administrative” area of Kibera

This method is acceptable since the building density is homogeneous throughout the slum. Yet, we can already assume that the result will be increased because the general Kibera boundaries comprises non building areas.

Given the number of inhabitants on the test sites (5359), the area of selected structures (3.73 ha) and the area for the whole Kibera (238 ha), we can derive the total estimated number of inhabitants for the entire Kibera = 341 942 inhabitants. We may infer a population density of 1437 people /ha.

#### Number of inhabitants per general inhabited area of Kibera

If we consider the only inhabited surface of Kibera (131.84 ha), we can derive a reduced number of inhabitants: 189 418 inhabitants. This result is likely to be more accurate because it benefits from finer data (inhabited surface). We may infer a population density of 1437 people /ha.

#### Number of inhabitants per number of structures in Kibera

If we consider the number of structures of the test sites (482) and of Kibera (17241), we can derive a reduced number of inhabitants: 191 690 inhabitants. We may infer an average number of person/structure equal to 11.

### Population estimate based on individual village estimates

The analysis by village is a means to reduce the error given the reduced size of the area under concern. This method requires the digitization of individual structures (roofs) prior to the analysis and is therefore the most time consuming method:

- Shapefile of the boundaries of Kibera villages (area in ha)

- Shapefile of all individual structures covering Kibera (inhabited area in ha)

- Field survey (visit of structures, people couting)

| KIBERA SLUM | Nb of Structures | Nb of units | Area of structures (ha) | Village area (ha) | Nb of inhabitants / nb structures | Nb of inhabitants / structure area | Nb of inhabitants / village area |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Gatwekera | 1978 | 7624 | 15.92 | 27.82 | 23053 | 24291 | 42449 |
| Kanbimuru | 446 | 1271 | 3.77 | 7.54 | 3367 | 3407 | 6801 |
| Karanja | 19 | 0 | 0.14 | 0.48 | 0 | 0 | 0 |
| Kianda | 1304 | 5154 | 9.68 | 16.29 | 17356 | 19653 | 33077 |
| Kisumu Ndogo | 886 | 4980 | 9.21 | 16.68 | 16437 | 15971 | 28925 |
| Laini Saba | 2193 | 5757 | 14.96 | 25.91 | 11342 | 12327 | 21348 |
| Lindi | 1931 | 5929 | 14.74 | 25.30 | 18666 | 21688 | 37221 |
| Makina | 2496 | 11422 | 21.86 | 43.55 | 31602 | 29248 | 58286 |
| Mashimoni | 825 | 4518 | 7.04 | 12.40 | 12375 | 12950 | 22815 |
| Olympic | 177 | 177 | 1.40 | 3.13 | 0 | 0 | 0 |
| Raila | 883 | 2060 | 4.01 | 8.13 | 6644 | 6464 | 13108 |
| Silanga | 1574 | 7630 | 12.51 | 20.76 | 15569 | 14193 | 23561 |
| Soweto East | 1939 | 9596 | 13.27 | 23.07 | 23566 | 18683 | 32478 |
| Soweto West | 590 | 2879 | 3.34 | 6.85 | 10360 | 8005 | 16437 |
| TOTAL – average of the results of all villages |  |  |  |  | 190337 | 186878 | 336506 |
| TOTAL – computation on basis of the general results | 17241 | 68997 | 131.84 | 238 | 191690 | 189280 | 341554 |

It has to be noted that population estimates differ according to the reference used to compute the total number of people.

- On basis of number of structures : 190 337 / 191 690 people

- On basis of structures surface: 186 878 / 189 280 people

- On basis of “administrative” area of each village: 336 506 / 341 554 people

The greater variation concerns the estimate based on the administrative area of each village which is overestimated by a factor 1.75 – 1.78 with regards to the other results.

### Population estimates based on the extrapolation of KIANDA results

In 2008, the Map Kibera Project (MKP), an independent international team, has conducted a thorough census in KIANDA village. The results are available on the Internet. Given the lack of precise census data over Kibera, we will consider their results as a good basis for validation.

The MSF estimates assessing the number of inhabitants per structures identified is close to that obtained by MKP.

| KIANDA | Kianda area (ha) | Nb of structures | Nb of inhabitants | Nb of units | KIBERA area (ha) | Pop density (pers/ ha) | Total estimated population |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Map Kibera Project | 16 | 1225 | 15219 | 5000 | 230 - 250 | 951.2 | 235000 to 270000 |
| MSF estimates / structures | 16.29 | 1304 | 17356 | 5154 | 238 | 1065.42 | 253570 |

If we apply the 7% of error to MSF’s results, we obtain a population between 235 820 and 271 320 inhabitants which is a very good estimate with regards to MKP figures.

Assessment of error:

| Error of MSF estimates / MKP | Percentage (+/- %) | Nb of elements |
| --- | --- | --- |
| identification of structures on the satellite imagery | 6 | + 79 |
| Identification of units | 3.08 | + 154 |
| Population estimates for KIANDA | 14.04 | + 2137 |
| Population estimates for KIBERA | 3.80 | + 9302 |

Considering the comparison, we can say that the results obtained on KIANDA by MSF are very good.

Therefore, we may infer that the results for the remaining villages have the same degree of accuracy. In the following table we applied the same method as the one used by MKP for population estimation:

Population density (= nb of inhabitant / village area) * Kibera area

| KIBERA SLUM | Village area (ha) | Nb of Structures | Nb of inhabitants | KIBERA area (ha) | Population density (pers / ha) | Total estimated population / each village |
| --- | --- | --- | --- | --- | --- | --- |
| Gatwekera | 27.82 | 1978 | 23053 | 238 | 828.63 | 197214 |
| Kanbimuru | 7.54 | 446 | 3367 | 238 | 446.86 | 106354 |
| Karanja | 0.48 | 19 | 0 | 238 | 0 | 0 |
| Kianda | 16.29 | 1304 | 17356 | 238 | 1065.42 | 253569 |
| Kisumu Ndogo | 16.68 | 886 | 16437 | 238 | 985.56 | 234564 |
| Laini Saba | 25.91 | 2193 | 11342 | 238 | 437.77 | 104190 |
| Lindi | 25.30 | 1931 | 18666 | 238 | 737.66 | 175563 |
| Makina | 43.55 | 2496 | 31602 | 238 | 725.57 | 172685 |
| Mashimoni | 12.40 | 825 | 12375 | 238 | 998.02 | 237528 |
| Olympic | 3.13 | 177 | 0 | 238 | 0.00 | 0 |
| Raila | 8.13 | 883 | 6644 | 238 | 817.16 | 194484 |
| Silanga | 20.76 | 1574 | 15569 | 238 | 749.97 | 178493 |
| Soweto East | 23.07 | 1939 | 23566 | 238 | 1021.50 | 243118 |
| Soweto West | 6.85 | 590 | 10360 | 238 | 1512.84 | 360057 |
| TOTAL – average of the results of all villages | 238 | 17241 | 190337 | 238 | 860.58 | 204818 |
| TOTAL – computation on basis of the general results | 238 |  | 191690 | 238 | 800.04 | 190410 |

In the above table you can see that the estimate of the Kibera population on basis of the extrapolation of each village population gives mixed results. This may mean that field data / digitization were not of equal quality on every village.

The average of those results provides a total estimate of 190 410 or 204 818 inhabitants depending whether we compute the estimates on basis of the general results or on basis of the average of all the estimates by village. This result is quite close to the population estimate based on the addition of extrapolated number of inhabitants per villages which amounts to 190 337 – 191 690 inhabitants.

## Results summary

|  | Nb People / nb structures | Nb People / Built surface | Nb People / ‘administrative’ area | Nb People / density (on basis of people/nb structures |
| --- | --- | --- | --- | --- |
|  | Raw result | +7% error | Raw result | +7% error | Raw result | +7% error | Raw result | +7% error |
| Per village | 190 337 | 203 661 | 186 878 | 199 959 | 341 942 | 365 878 | 204 818 | 219 155 |
| Kibera | 191 690 | 205 108 | 189 418 | 202 677 | 336 504 | 360 059 | NA | NA |
| Kianda extrapolation MKP | NA | NA | NA | NA | Mean value 244268 | 235 000 – 270 000 | NA | NA |
| Kianda extrapolation MSF | NA | NA | NA | NA | 253 570 | 271 320 | NA | NA |

## Conclusion:

We will take into consideration the results with the 7% error.

Population estimates based on the ‘administrative’ boundaries are overestimated by a rough 1.75 factor with an average value of 362 969 people.

Population estimates based either on the number of structures or the built surface are quite coherent and range from 199 959 to 205 108 people with an average of 202 533 people.

With regards to the thorough field survey from MKP, MSF data appear to be very coherent which means that the method used – a combination of remote sensing interpretation and mapping and field random field survey – seems valid. It should be further validated though by comparing the results for other villages, yet MKP has not started with the rest of the slum.

Results extrapolated from Kianda data amount to 253 570 people for the whole Kibera. Results extrapolated from each individual villages based on the Kianda method amount to 204 818 people.

We may assume that results based on the built surface is more accurate than the results based on the general ‘administrative’ areas that contain unbuilt areas like roads, rivers … The results that are to be considered range thus from 199 959 to 202 677 with an average of 201 338 people for the entire Kibera. This figure is lower than the estimate obtained by MKP.

# Footnotes

http://www.imcworldwide.org/images/Image/Kenya/kenya04_kibera.jpg

For references, see Monitoring of Urban Growth of Informal Settlements and Population Estimation from Aerial Photography and Satellite Imaging by G. Sartori, G. Nembrini and F. Stauffer. Mapping the Unmapped by Stefano Marras from the ongoing Map Kibera Project.

The HUMAN project was financed by the European Space Agency and carried out by Keyobs for MSF-B. It developed mapping support for MSF activities and emergency interventions.

RPC provide

Results in blue were extrapolated from field data

http://www.mapkiberaproject.org/

1225 main structures identified among 1500 buildings counted in Kianda. 300 smaller structures are public toilets or baths which are likely to be missing among the structures extracted from the satellite imagery because of their reduced size.

Dr Stefano Marras extrapolated the results of Kianda to Kibera at large on basis of the population density taking into account an estimated error of 7% (“We can guess this estimate multiplying the population density found in Kianda for the area of Kibera taking into account an estimated error of 7%”).

Dr Stefano Marras extrapolated the results of Kianda to Kibera at large on basis of the population density taking into account an estimated error of 7% (“We can guess this estimate multiplying the population density found in Kianda for the area of Kibera taking into account an estimated error of 7%”).

The formula used to assess the % of error is the following: computed value/reference value*100= % of precision-100= % of error.

The average estimation considered for MKP is based on the average area for Kibera of 240 ha thus making the population estimates up to 244268 people (included the 7% error factor).

Results in blue were extrapolated from field data

The number of inhabitants based on the number of structures is the closest one to the population figure obtained by MKP. Therefore we chose this one for our analysis.